## Slide 1: IOT based Dual Mode Fire Extinguishing Robot
Submitted by : Gurvinder Singh Submitted to : Prof. Mike Aleshams
Student id-748418

## Slide 2: Contents
Abstract
Proposed System
Flow Chart
Dual Mode
Description
Hardware
Conclusion
References

## Slide 3: Abstract
Development of dual mode(automatic and manual) firefighting robot .
Operation of robot is monitored by Arduino UNO microcontroller.
Surveillance camera is used.
Manpower is required in manual mode.

## Slide 4: Proposed System

## Slide 5: Flow Chart

## Slide 6: Automated Mode
Robot is completely automated to search for the presence of possible flames and obstacles.
The robot moves around and search for the signs of flame. In the case of the presence of an obstacle in the path of the robot, it will deviate to right until the obstacle is clear of its path.
This is done using an ultrasonic sensor attached to the robot.
It wirelessly sends the information to the authorities regarding the fire.
Once the pumping action is initiated, the motor for the pump will be enabled and sprays the water. This is done until the flame is bought down to ground level.

## Slide 7: Manual Mode
To operate the robot in manual mode, a Bluetooth module is used.
System is connected to smart phones by using a Bluetooth module. The Bluetooth device can be configured to receive corresponding serial data for controlling the robot which is transmitted from the smartphone.
An override button and switch button is configured to switch between the two modes of operation of the robot.
The movement and pumping action of the robot can be controlled with the help of the configured smartphone.

## Slide 8: Description
Firefighting robot has three flame detectors(Two long range and one short range sensor).
Long range sensor(range 400m) and Short range sensor(200m).
Flame sensor used is LM393.
Bluetooth module and Surveillance camera is used for obstacle detector.
Arduino UNO microcontroller is used to operate the robot as it receives the information from the sensors.

## Slide 9: Hardware
Arduino UNO microcontroller is used to control the process of the robot.
Bluetooth module is used to operate the robot from remote location in wireless mode.
Version 2.0 Bluetooth protocol is used to communicate between robot and the remote.
This is a microcontroller board based on ATMega 328. It has 14 digital input/output pins (of which 6 can be used for PWM outputs), 6 analog inputs, a 16Mhz ceramic resonator, a USB connection, a power jack, an ICSP header, and a reset button.
The flame sensor is connected to the analog input pins in the Arduino.

## Slide 10: Conclusion
A dual mode firefighting robot which works in both automated and manual mode.
Arduino microcontroller is used as the processing and control unit of the robot.

## Slide 11: References
Sheikh Mohammed S, Joyal Raju. (2017), “Development and Implementation of Arduino Microcontroller based dual mode fire extinguishing robot” IEEE International Conference on Intelligent Techniques in Control, Optimization and Signal Processing.