## Slide 1: IOT based Dual Mode Fire Extinguishing Robot with Modifications
Submitted by : Gurvinder Singh Submitted to : Prof. Mike Aleshams
Student id-748418

## Slide 2: Contents
Abstract
Proposed System
Dual Mode
Modifications
Conclusion
References

## Slide 3: Abstract
Development of dual mode(automatic and manual) firefighting robot .
Operation of robot is monitored by Arduino UNO microcontroller.
Surveillance camera is used.
Manpower is required in manual mode.

## Slide 4: Proposed System

## Slide 5: Automated Mode
Robot is completely automated to search for the presence of possible flames and obstacles.
The robot moves around and search for the signs of flame. In the case of the presence of an obstacle in the path of the robot, it will deviate to right until the obstacle is clear of its path.
This is done using an ultrasonic sensor attached to the robot.
It wirelessly sends the information to the authorities regarding the fire.
Once the pumping action is initiated, the motor for the pump will be enabled and sprays the water. This is done until the flame is bought down to ground level.

## Slide 6: Manual Mode
To operate the robot in manual mode, a Bluetooth module is used.
System is connected to smart phones by using a Bluetooth module. The Bluetooth device can be configured to receive corresponding serial data for controlling the robot which is transmitted from the smartphone.
An override button and switch button is configured to switch between the two modes of operation of the robot.
The movement and pumping action of the robot can be controlled with the help of the configured smartphone.

## Slide 7: Modifications
A variety of lower-end and higher-end sensors were grouped together in sensor packages, and evaluated based on a set of cost and performance criteria.
System comprised of a high-end Net Safety Triple IR flame detector, a USB night vision web camera, a Hamamatsu UVTron flame detector, and a combination photoelectric-ionization smoke alarm can be used for better and fast performance.
These sensors readings are all to be evaluated in parallel in order to have built in redundancy when deciding to sound a fire alert. This enables the reduction of false alarm signals, and allows for the detection of most common fires (class A fires).

## Slide 8: Modifications
The control circuit of the proposed fire extinguishing robot is modeled and simulated using Proteus 8.8.
A microcontroller board based on ATMega 328 can be used as It has 14 digital input/output pins (of which 6 can be used for PWM outputs), 6 analog inputs, a 16Mhz ceramic resonator, a USB connection, a power jack, an ICSP header, and a reset button.
Obstacle sensor used in the robot is HCSR04 ultrasonic sensor to improve performance to avoid obstacles.
Sonar may be used to measure distance to an object it offers excellent range accuracy and stable readings in an easy-to-use package.

## Slide 9: Modifications
Robot movement is controlled by two motors, Motor Driver IC’s act as an interface between the microcontroller and the motors of the robot.
Motor Driver IC L293D is a dual H bridge driver.

## Slide 10: Conclusion
Performance is yet to be confirmed through testing however, there is a fair amount of certainty that the overall system will perform adequately due to the built in redundancy of sensor package.

## Slide 11: References
Sheikh Mohammed S, Joyal Raju. (2017), “Development and Implementation of Arduino Microcontroller based dual mode fire extinguishing robot” IEEE International Conference on Intelligent Techniques in Control, Optimization and Signal Processing.